DECORLUX

DESCRIPTION

Decorlux is a ready-mixed marble finish for interior use.  It is a pure mineral product.  The main component is conditioned lime putty manufactured from selected raw materials.

TECHNICAL PROPERTIES

Specific density		approx. 1.7 kg/litre

Dilution			ready to use, can be diluted with water

COVERAGE

0.3 to 1 kg/m2, depending on the base

COLOUR

The product is supplied in natural white and in 20 ready-mixed shades.  The Coridecor oxide colour concentrates can be used to produce any colour you want.

USE

Preparation

Corifondo should be applied as a base coat before using Decorlux on synthetic and gypsum backgrounds.  This primer is a base coat material for the Coridecor stucco products.  The primer provides a base, which will absorb Decorlux evenly and give a good bond.  Vapour permeability is also maintained.  Corifondo can be diluted with water (20 to 50%), depending on the absorption capacity of the base.  Corifondo can also be coloured with the oxide colour concentrates so that the first colour can be applied as early as the base coat.

Types of base

. Gypsum, lime, lime-cement and cement plasters

First remove dust parts from the plasterwork, next cover with primer or thin plaster and then apply Corifondo as the base coat.

. Concrete

Concrete should be pre-treated with a suitable primer before applying Corifondo as the base coat.

. Gypsum plasterboard, chipboard

Gypsum plasterboard and chipboard must be rendered flat and smooth with a suitable primer or plaster, before applying Corifondo as the base coat.

The base must be absolutely dry and form a stable background before the base coat is applied.  Loose or peeling paint, lime paint and distemper should be removed. Allow the Corifondo to dry thoroughly (12 hours) before starting to apply Decorlux.

How to use Decorlux

Apply Decorlux with the flexible 80 x 200 trowel from the stainless steel 120 x 280 trowel.  Apply in small quantities (to cover), at least three times.

Once the surface is perfect, you can start polishing.  Again the right tool is particularly important.  Clean the flexible trowel with 300 grit sandpaper.  It is recommended that you do not apply a final coat of wax to Decorlux surfaces.  The surface will shine without wax and can always be patched.  Coridecor Plastelux can be used where washable surfaces are required (restaurants, hotels, public buildings and high-moisture rooms).

Of the Oxide colour paint concentrates, only the oxide concentrates types E1 to E6 can be used for Decorlux.  These are lime-resistant and light fast.

RL6	oxide-yellow			RL10	oxide-black

RL8	oxide-red			RL5	oxide-blue

RL7	oxide-brown			RL9	oxide-green

(packaged in 500 ml dropper bottles)

PACKAGING

25 kg and 5 kg plastic buckets.

NOTES

Because of the composition of the product (lime), avoid contact with the skin and particularly with the eyes.  Rinse eyes immediately with plenty of water and seek medical advice.  Keep out of reach of children.

Decorlux is not suitable for high-moisture rooms or exterior use.

Decorlux should be stored in a cool, dry place, at a minimum temperature of 3°C.  The product will then keep for an unlimited period in its original packaging.

Once opened, the packaging should be hermetically sealed again after use.

MARMOLUX

DESCRIPTION

Marmolux is a marble finish made from lime putty, carefully selected powdered marble and vegetable additives.  Its porous structure means Marmolux is vapour-permeable.

The surface has a smooth, shiny and marble-like appearance of high aesthetic quality.

APPLICATIONS

Because of its properties and qualities Marmolux is suitable both for restoring old, historical buildings and in modern architecture.

Marmolux is frost-resistant and can be used indoors or out.

TECHNICAL PROPERTIES

Coverage		0.5 to 1 kg/m2

Specific density	1.7 kg/dm3

Drying time		7 to 8 hours, depending on weather conditions

Fully hardened	after 6 to 9 months

BASE

Marmolux should preferably be applied to a fine lime mortar, without a bonding coat.  It can also be used on a cement or gypsum base.

USE

Before applying Marmolux, the base should be dampened down slightly prior to overcoating.  Marmolux is ready to use but should be stirred first.  Apply with a stainless steel plastering trowel to a thickness of max. 0.2 to 0.3 mm.  Apply the second coat, also to a max. Thickness of 0.2 to 0.3 mm, before the first coat is completely dry.  Apply firm pressure to this coat, using criss-cross movements.  Repeat pressure several times, depending on the required appearance (smooth or satin). Once the Marmolux coats are dry, start to polish with a clean stainless steel plastering trowel.  For a perfectly smooth surface finish, polish once again with a woollen cloth.

PACKAGING

25 kg and 5 kg plastic buckets.

NOTES

Marmolux should be stored in a cool, dry place, at a temperature above 3°C.  The product will then keep for an unlimited period in its original packaging and will retain its properties.  Once opened, the packaging should be hermetically sealed again after use.

In the event of direct contact with the skin : wash thoroughly with soap and water.  In the event of contact with the eyes, rinse thoroughly with plenty of water and seek medical advice.  Keep out of reach of children.

Our advice and instructions are always given in good faith.  We guarantee the consistent quality of our products but we cannot accept any liability with regard to their use.  If you have any queries, please contact our technical department.

PLASTELUX

DESCRIPTION

Plastelux is made from special, high-quality resin, mineral products, fillers, oxide pigments and various additives.  The decorative chip technique of Plastelux gives walls and ceilings a particularly aesthetic appearance, with a refined and elegant ambience.  The surface is smooth and glossy, graceful in form, rich in colour effects, structures and light-shade nuances.

The use of Stucco Lucido (masterpieces) originated in ancient times but reached its peak in the Renaissance and Baroque periods, particularly in the Venice region.  Plastelux is the splendid result of the rich experience of the stucco masters of that period. The particular properties of the stucco materials have been further refined by the use of modern production techniques.

APPLICATIONS

All types of interior, even quite high-moisture rooms, as the product is water-resistant and washable.

TECHNICAL PROPERTIES

Specific density		approx. 1.650 kg/litre

Dilution			ready-mixed, with oil of turpentine

COVERAGE

0.3 to 1.0 kg/m2, depending on the base.

COLOUR

Supplied ready-mixed in white.  Can be coloured using Coridecor oxide colour concentrates by mixing in an agitator.  There are also 8 ready-mixed shades available.  Special shades can be produced in the factory from colour samples.

USE

Plastelux can be used without any problem on almost any base, after the appropriate pre-treatment : on all types of new or painted plasterwork, concrete, plasterboard and wood bases and with a special primer on plastic (coatings) and metal.

Pre-treatment is not necessary if the base is plastered with plain plaster.

But if the plaster contains gypsum or has already been painted, a base coat of Corifondo should be applied.  If the base is not a stable background or comprises several coats of paint, lime paint or washable paint, it should be made smooth.  Residues should be removed and a base coat of Corifondo must be applied.  Wood bases must be treated with Corifondo wood impregnator. 2 to 3 coats of Plastelux should be applied, depending on the condition of the base, using a special flexible trowel made of spring band steel, until the surface is completely smooth and homogenous.  The flexible trowel or a palette knife is then used to produce the required surface structure.  To achieve the characteristic and typical effect of the Venetian plaster, Stucco Lucido, the product should be applied until a uniform and perfect gloss finish is achieved.  The same tool can be used for polishing the surface as for applying the product.  Another option is to use a cotton cloth.  If Plastelux is used as a final coat, the base coat can be Venestuk.

If, for the last application, Plastelux is applied on top of Venestuk, there is no need to apply wax.  Plastelux is washable and dirt-repellent and can be treated in the same way as a lacquered surface.

A waxed stucco surface can only be repaired to a limited extent.  Plastelux can be easily patched and reapplied without leaving streaks.

PACKAGING

5 kg and 25 kg buckets.

NOTES

Because of the composition of the product (lime), avoid contact with the skin and particularly with the eyes.  In the event of contact rinse eyes immediately with plenty of water and seek medical advice.  Keep out of reach of children. Plastelux should be stored in a cool, dry place, at a minimum temperature of 3°C.  The product will then keep for an unlimited period in its original packaging and will retain its properties.  Once opened, the packaging should be hermetically sealed again after use.

VENESTUK

DESCRIPTION

Venestuk is made from a base of high-quality, vegetable components, lime putty, carbonates, mineral colour pigments and various additives to simplify use. The decorative chip technique of Venestuk gives walls and ceilings a particularly aesthetic appearance, with a refined and elegant ambience.  The surface is smooth and glossy, graceful in form, rich in colour effects, structures and light-shade nuances.

The use of Stucco Lucido (masterpieces) originated in ancient times but reached its peak in the Renaissance and Baroque periods, particularly in the Venice region.  Venestuk is the splendid result of the rich experience of the stucco masters of that period. The particular properties of the stucco materials have been further refined by the use of modern production techniques.

TECHNICAL PROPERTIES

Specific density		approx. 1.750 kg/litre

Dilution			ready-mixed, dilute with water

COVERAGE

0.3 to 1.5 kg/m2, depending on base.

COLOUR

Supplied ready-mixed in white.  Can be coloured using Coridecor-oxide colour concentrates by mixing in an agitator.  There are also 8 ready-mixed shades available.  Special shades can be produced in the factory from colour samples.

USE

Venestuk can be used without any problem on almost any base, after the appropriate pre-treatment : on all types of new or painted plasterwork, concrete, plasterboard and wood bases and with a special primer on plastic (coatings) and metal.

Pre-treatment is not necessary if the base is plastered with plain plaster.  But if the plaster contains gypsum or has already been painted, a base coat of Corifondo should be applied.  If the base is not a stable background or comprises several coats of paint, lime paint or washable paint, it should be made smooth.  Residues should be removed and a base coat of Corifondo must be applied.  Wood bases must be treated with Corifondo wood impregnator.

2 to 3 coats of Venestuk should be applied, depending on the condition of the base, using a special flexible trowel made of spring band steel, until the surface is completely smooth and homogenous.  The flexible trowel or a palette knife is then used to produce the required surface structure.  To achieve the characteristic and typical effect of the Venetian plaster, Stucco Lucido, the product should be applied until a uniform and perfect gloss finish is achieved.  The same tool can be used for polishing the surface as for applying the product.  Another option is to use a cotton cloth.  If Plastelux is used as a final coat, the base coat can be Venestuk.

Venestuk can be given extra protection against dirt with Coridecor wax protector : this makes Venestuk washable.  The wax cannot be applied to the Venestuk surfaces until 10 days after completion.

A waxed stucco surface can only be repaired to a limited extent.  Plastelux can be easily patched and reapplied without leaving streaks.

PACKAGING

5 kg and 25 kg tubs.

NOTES

Because of the composition of the product (lime), avoid contact with the skin and particularly with the eyes.  In the event of contact rinse eyes immediately with plenty of water and seek medical advice.  Keep out of reach of children.

Venestuk should be stored in a cool, dry place, at a minimum temperature of 3°C.  The product will then keep for an unlimited period in its original packaging and will retain its properties.  Once opened, the packaging should be hermetically sealed again after use.